Aero-Sensors Module
Manufacturing and Ordering
For: Aero Sub-System Validation
Lead: Philippe Grimard
Designer: Joshua Lafleur
Date: July 31st, 2022

TABLE OF CONTENTS
1.	JLCPCB MANUFACTURING AND ASSEMBLY	4
2.	ELCTRONIC COMPONENTS OREDERING	5

1. JLCPCB MANUFACTURING AND ORDERING

1.	Goto JLCPCB (https://jlcpcb.com/)
2.	Click on “Add gerber file” and upload gerbers.zip
3.	Select 2 Layers
4.	PCB Qty: 5
5.	Delivery Format: Single PCB
6.	PCB Thickness: 1.6
7.	Select PCB Assembly
7.1	PCBA Type: Economic
7.2	Assembly Side: Top Side
7.3	PCBA Qty: 2
7.4	Tooling holes: Added by JCLCPCB
7.5	Confirm Parts Placement: Yes
8.	Click Next
9.	Add BOM File and upload aero_sensors_bom_jlcpcb.csv
10.	Add CPL File and upload aero_sensors-top-pos.csv
11.	Select correct usage → Sensor\Controller\Precision Instrument →
Pressure Sensor
12.	Confirm Inventory shortage on MAX7356EUG+ and MPRLS0025PA00001A	ONLY
13.	Click NEXT
14.	Order ready to be placed
2. ELECTRONIC COMPONENTS ORDERING

Part Number	Supplier Part Number	Qty	Supplier
PCBM (5 boards) PCBA (2 boards)	See Previous Section	1	JLCPCB
0022272041	WM4113-ND	30	DigiKey
0022122044	WM2713-ND	18	DigiKey
0050579504	WM2878-ND	50	DigiKey
0008510108	WM19393CT-ND / Cut Tape (CT)	200	DigiKey
MPRLS0025PA00001A	480-7098-1-ND / Cut Tape (CT)	16	DigiKey
MAX7356EUG+	MAX7356EUG+-ND	3	DigiKey
NPA-700B-030D	45-NPA-700B-030DCT-ND / Cut Tape (CT)	1	DigiKey